## Slide 1
Using Mobile Phones to Write in Air

## Slide 2
Who and Where?
 Systems Networking Research Group
Duke University, Durham, NC, 2009 - 2011

## Slide 3
Introduction/motivation:
What was the main problem addressed?
 MOTIVATION:
 Phones and sensors allow for people-centric apps. Can write in the air.
 MAIN POBLEM:
 Alternative input method using accelerometer for text and drawing by writing in the air - use mobile phone to write in the air

## Slide 4
Introduction/motivation:
What was the main problem addressed?
 WHY IMPORTANT:
 Assistive technology - Allow people with disabilities to use
 Don’t have to type, frees your other hand and your eyes to watch what’s around you.
 Writing English alphabets/words in real-time with
commodity phones has been an unexplored problem.  http://www.youtube.com/watch?v=Nvu2hwMFkMs

## Slide 5
Introduction/motivation:
Why is this problem solved important?
 VISION:
 PhonePoint Pen (P3) establishes feasibility and justifies longer-term research commitment
 Write short messages, draw simple diagrams  Use cases
 Assistive technology for impaired patients  Equations and sketching
 Emergency operations and first responders  Write message on top of picture

## Slide 6
Related Work:
Vision based gesture recognition
 Use cameras to track object’s 3D movements  TinyMotion
 Uses built-in cell phone camera to detect simple movements.
 No character or word detection.
 Microsoft Research TechFest: Write in The Air (2009)
 Character, but no word detection.
 http://www.youtube.com/watch?v=WmiGtt0v9CE

## Slide 7
Related Work:
Stylus-based sketch recognition
 Draw sketches on a pad or Tablet PC using a stylus
 SketchREAD
 Electronic Cocktail Napkin
 Unistrokes - single-stroke characters  Graffiti - single-stroke characters  Pen-touch based Tablet PCs
 Can relocate pen
 Visual reference
 Samsung Galaxy Note (5”, 8”, 10”)

## Slide 8
Methodology:
Overview/Summary of approach/design
 Nokia N95 phone (2007)
 Symbian OS
 Experiments with
 10 CS and Engineering students
 Novice (<10 chars)
 Trained (>26 chars)
 5 patients from Duke University Hospital

## Slide 9
Methodology:
Core Challenges - Rotation Gyroscope
ISSUE:
 Nokia N95: cannot detect rotation
3-axis accelerometer X, Y, Z, no gyroscope
 Can’t tell difference between linear movements and rotation using just the accelerometer.

## Slide 10
Methodology:
Core Challenges - Rotation Gyroscope
APPROACH:
 Hold like pen or blackboard eraser
 Pause between strokes

## Slide 11
Methodology:
Core Challenges - Background Vibration
ISSUE:
 Jitter from natural hand vibrations
 Measurement errors from accelerometer APPROACH:
 Noise-reduction
 Smooth with moving average over last 7 readings  Drop data under threshold, <= 0.5m/s2 = noise

## Slide 12
Methodology:
Core Challenges - Computing Displacement
ISSUE:
 Phone movement can introduce errors as integrating from Acceleration to velocity to displacement.
APPROACH:
 Reset velocity to zero if previous accelerometer readings below threshold (noise)

## Slide 14
Methodology:
Core Challenges - “A” v. Triangle
ISSUE:
/
+
\
+
= A … or a triangle?
APPROACH:
 Watch for “lifting of the pen”
 Monitor data, but don’t include in final output

## Slide 15
Methodology:
Core Challenges - Character Transitions
ISSUE:
 Can’t tell difference between B and 13 same set gestures cause ambiguities
APPROACH:
 Use delimiter between characters - dot or pause
B =
13 =

## Slide 16
Methodology:
Gesture Stroke Detection primitives

## Slide 17
Methodology:
Character Recognition
 Stroke grammar using decision tree
 D and P - start same, but then can turn into N  O and S - same strokes
 X and Y - same strokes
 O and 0 - cannot tell difference

## Slide 18
Methodology:
Stroke grammar for English alphabets and digits
Single gesture
Intermediate state
Final state

## Slide 20
Methodology:
Word Recognition
 Examples: B and 13, H and IT
 Look at sequence of previous and next strokes  Infer previous character when see start of new char
 Watch for move back to left position
 Have user pause or draw dot to delimit characters

## Slide 21
Methodology:
P3-Aware Spelling Correction
 Distance for correction (replace # chars)
 MQM edit distance of 1 with MOM, MAM, MUM.
 P3 confuses Q with O but hardly confuses Q with A or U, can suggest MOM with high confidence.
 NIET - could be NET or MET
 Edit distances of 1 and 2,
 P3 confuses “M” as “NI” > probability than “E” as “IE”. could predict user intended MET with reasonably high probability

## Slide 22
Methodology:
P3-Aware Spelling Correction
Probability of valid word i
Corrected word
Probability of valid word j

## Slide 23
Methodology:
Assumptions and limitations of this work
 Speed of writing = 3:02 sec/letter on average  Repositioning pen for long words and drawing  Cursive handwriting (continuous movement)  Can’t write AND move at same time  Users were CS majors, but can train others  Investigate “greater algorithmic sophistication” for gesture recognition (Bayesian Networks and Hidden Markov Models)

## Slide 24
Results:

## Slide 25
Results:
 English characters identified with average accuracy of 91:9% … but
 Slow: speed = 3.02 sec

## Slide 26
Results:

## Slide 27
Results:
Human Readability Accuracy (HRA)
Average readability
 Trained writers: 83%  Novice writers:85:4%

## Slide 28
Results:
Character Recognition Accuracy (CRA)
Average character recognition (stroke grammar)  Trained writers: 91:9%
 Novice writers: 78:2%

## Slide 30
Results:
Character disambiguation
Common set of strokes causes confusion
correct

## Slide 31
Results:
Median time to correctly write character
 4.3 sec (all)
 3.02 sec (min)

## Slide 32
Results:

## Slide 33
Results:

## Slide 34
Results:
Hospital Patients
 Only 5 patients
 Cognitive disorders and motor impairments  Write 8 random letters
 Not allowed to observe patients  Problem pressing button
 Suggestions from doctors: Try left-hand to emulate speech-impaired patients.

## Slide 35
Discussions/Conclusions/Future Work
 Not extensive, only 10 students, 5 patients  Prototype, shows possibilities
 Improve prototype, new user-experience “that complements keyboards and touch-screens.”
 Integrate gyroscope in next PhonePoint Pen
 TEDxDuke - Vansh Muttreja on the Virtual White Board - A New Way of Remote Collaboration
 http://www.youtube.com/watch?v=vmyXJzkfevY

## Slide 36
Discussions/Conclusions/Future Work
 Some other ideas
 Use back camera to optically track movement?  Write in the air
 Geo-location
 Augmented reality

## Slide 37
References
 PhonePen Video
http://www.youtube.com/watch?v=Nvu2hwMFkMs
 Systems Networking Research Group (at Duke University) http://synrg.ee.duke.edu
 LiveMove Pro: Advanced Motion Recognition http://www.ailive.net/liveMovePro.html
 Zhen WANG - uWave
http://www.owlnet.rice.edu/~zw3/projects_uWave.html  Nokia N95
http://en.wikipedia.org/wiki/Nokia_N95  Symbian mobile operating system http://en.wikipedia.org/wiki/Symbian_OS

## Slide 38
References
 Leap Motion Controller
https://www.leapmotion.com/
 Magic : Write This Down in Air into your iPhone (using a magnet) http://www.youtube.com/watch?v=W89cpE9gFMg
 Writing in the Air for Google Glass (MessagEase)
http://www.youtube.com/watch?v=wfmlNuPwmS0  Bayesian network
http://en.wikipedia.org/wiki/Bayesian_network  Heuristic
http://en.wikipedia.org/wiki/Heuristic

## Slide 39
Questions?