## Slide 1: Introduction to Smartphone Energy Management

## Slide 2: Issue 1/2
Rapid expansion of wireless services, mobile data and wireless LANs
Greatest limitation: finite power supplies

## Slide 3: Issue 2/2
Typical example of power consumption from a mobile device:
  36% Display
  21% CPU/memory
  18% Wireless
  interface
  18% Hard drive
Goal
  Incorporate energy conservation at all layers of protocol stack

## Slide 4: Energy Efficiency Research in Protocol Stack

## Slide 5
Two different perspectives
Increase battery capacity
  Increase capacity while restricting weight
  However battery technology hasn’t experienced significant advancement in the past 30 years
Decrease of energy consumed
  Run CPU at lower clock rate, lower voltages
  Flash memory (SD (Secure Digital) Memory Card)

## Slide 6: Datalink Layer Battery Management
Lazy Packet Scheduling: Reduce the power  Increase the transmission time
Battery-Aware MAC Protocol: Packets carry remaining charge. Lower back off interval for nodes with higher charge

## Slide 7: Network Layer Battery Management
Goal: Increase the lifetime of the network
Shaping: If battery charge becomes below threshold, stop next transmission allowing battery to recover
Battery Energy Efficient (BEE) Routing Protocol: Minimize energy and use max battery charge

## Slide 8: Sources of Power Consumption
Two types
  Communication related
  Computation related
Tradeoff between them

## Slide 9: Communication related
Three modes:
  Transmit
  Receive
  Standby
Example:
  Proxim RangeLAN2 2.4 GHz 1.6 Mbps PCMCIA card 1.5W transmit, 0.75W receive, 0.01W standby
Turnaround between transmit and receive typically takes 6 to 30 microseconds
Optimize the transceiver usage

## Slide 10
Power Management Modes
Power consumption is always an issue with Mobile Devices.
There are 3 modes of power for Cisco NIC cards:
Constant Awake Mode (CAM)
  Mode is best when power is not an issue such as when AC power is available to the device. Default mode
Power save mode (PSM)
  Mode is used when power conservation is the utmost importance. The wireless NIC card will go to ‘sleep’ after a period of inactivity & periodically awake to retrieve buffered data from the AP.
Fast power save mode (FastPSM)
  Combination of CAM & PSPM For clients who switch between AC & DC power.
Notes: Self explanatory

## Slide 11: Computation related
Usage of CPU, main memory and disk
Data compression techniques for reduction of packet length increase power consumption

## Slide 12: General Guidelines and Mechanisms 1/5
Reduce collisions in MAC
  Retransmissions lead to power consumption and delays
  Cannot be completely eliminated due to user mobility and varying set of mobiles
Change typical broadcast mechanism
  802.11: Receiver keeps track of channel status through constant monitoring

## Slide 13: General Guidelines and Mechanisms 2/5
Turnaround between transmit and receive mode spends time and power
  Allocate contiguous slots for transmission or reception
  Request multiple transmission slots with a single reservation packet
Computation of transmission schedule should be relegated to base station

## Slide 14: General Guidelines and Mechanisms 3/5
Scheduling algorithm may additionally consider battery power level
Allow mobile to re-arrange allocated slots under low-power conditions
At link layer:
  Avoid transmissions when channel conditions are poor
  Combine ARQ (Automatic Repeat Request) and FEC (Flow & Error Control) mechanisms

## Slide 15: General Guidelines and Mechanisms 4/5
Energy efficient routing protocols
  Ensure all nodes equally deplete their power level
  Avoid routing through nodes with lower battery power
    Requires mechanism for dissemination of node battery power
  Periodicity of routing updates can be reduced
    May result in inefficient routes

## Slide 16: General Guidelines and Mechanisms 5/5
OS level
  Suspension of specific sub-unit (disk, memory, display etc.) when detect prolonged inactivity

## Slide 17: Summary
Battery Management: idling increases the capacity of the battery
Transmission Power Management: Time/Signal Strength vs. Power tradeoff
System Power Management: Put system/components to sleep whenever possible