## Slide 1: Computer Networking Industry Perspective
IIT Kharagpur, Spring 2017
Amit Saha

## Slide 3: Connecting to a WiFi Access Point
Scanning
Joining
Authentication
Association
The station feels as if it is “plugged” into a wired network
Notes: Use acrylic wifi program to show ssids that are visible right now

## Slide 4: Communicating with a WiFi AP
Wireless is a half duplex channel – either speak or listen
  Signal strength is inversely proportion to square of distance
Carrier Sense Multiple Access / Collision Avoidance (CSMA/CA)
  Fancy name for how humans talk 
This is generally true of all wireless systems (including humans)
Notes: Draw out RTS/CTS or simply DATA/ACK

## Slide 5: WiFi Equipment

## Slide 6: Wired First Hop - Ethernet
IEEE 802.3 standard
If two ends of the Ethernet cable (e.g., RJ45) is electrically up, connection is up.
  Some authentication steps are usually there but we will skip those

## Slide 7: CSMA/CD
Carrier Sense Multiple Access / Collision Detect
Notes: Minimum size frame

## Slide 8: Ethernet Frame – with VLAN
88 bytes minimum
Notes: Minimum size frame

## Slide 9: Main issue in Ethernet
Loop prevention – for multiple VLANs
STP, MSTP

## Slide 10: Ethernet Equipment

## Slide 11: Getting an IP address
DHCP – DHCP clients get IP addresses and networking parameters from DHCP server
Based on BOOTP
DHCPv6 (for IPv6) is also available

## Slide 12: DHCP Packets
Discovery
Offer (possibly multiple)
Request
Acknowledge
Renew
Release
Why do we need an IP address?
Notes: Ask why do we need a request and acknowledge and not just a discover and offer?

## Slide 13: IP Packet Format

## Slide 14: IPv4 Header Format

## Slide 16: TCP/UDP Header

## Slide 17: Got an IP! Hurray!
But now what? How do I “go to” some website?
IP is just an identity
Still need to “route” to somewhere

## Slide 18: Domain Name Service
We almost always try to reach a human readable name
But machines route based on IP addresses
There must be a mapping from names to IP addresses
But who is going to do this translation?

## Slide 19: Default Gateway
If host does not know how to route, who does it ask?
There must be a “goto” guy in the network

## Slide 20: Routing table – Host
ubuntu@ubuntu-VirtualBox:~/Projects/OpenStack/New/cinder$ route
Kernel IP routing table
Destination Gateway Genmask Flags Metric Ref Use Iface
default 10.0.2.2 0.0.0.0 UG 0 0 0 eth0
10.0.2.0 * 255.255.255.0 U 1 0 0 eth0

## Slide 21: Are we ready to send?

## Slide 22: ARP
What is the MAC address for a given IP?
ARP resolves network layer address to link layer address

## Slide 23: Layer in packet format
We can now send

## Slide 24: Homework
Wireshark
Download wireshark and capture packets to see for yourselves

## Slide 25: DNS – Domain Name Service
Hierarchical way of managing name space
Managed by Internet Assigned Numbers Authority (IANA)
http://www.iana.org/domains/root/db

## Slide 27: DNS – Root Servers
<a-m>.root-servers.net – 13 hostnames, around 500 instances
  Use anycast to reach “nearest” instance – BGP supports this
  12 of the 13 root servers A-M exist in multiple locations
  11 on multiple continents
    Root server ‘h’ exists in two U.S. locations.
    Root server ‘b’ exists in a single location in the Los Angeles Area
http://www.root-servers.org/

## Slide 28: Subnetting
Routing to each individual hosts does not scale
Addresses grouped into different classes

## Slide 29: CIDR
Any “class system” is bad 
IPv4 was running out of unique IP addresses
  Hence IPv6 but…
Classless Inter Domain Routing
  Network portion can be of any size
  Addresses need to specify subnet mask as well

## Slide 30: Route Lookup – Longest Prefix Match

## Slide 31
How are the packets with above three destination IP addresses forwarded?
1->D, 2->B, 3->B
1->D, 2->B, 3->D
1->B, 2->D, 3->D
1->D, 2->D, 3->D

## Slide 32: Longest Prefix Match

## Slide 33: Route Lookup – Longest Prefix Match

## Slide 34
How are the packets with above three destination IP addresses forwarded?
1->D, 2->B, 3->B
1->D, 2->B, 3->D
1->B, 2->D, 3->D
1->D, 2->D, 3->D

## Slide 35: Longest Prefix Match

## Slide 36: Real Products

## Slide 41: RJ45 Port and Connector
Copper

## Slide 42: SFP and QSFP
Fiber Optic
Higher Capacity

## Slide 49
Replication Engine | Frames that must be sent to multiple ports are duplicated and dispatched from this chip as needed (more below)
Forwarding Engine | This is the chip with TCAM lookup tables and makes the routing and/or switching decisions. In other words, a table of addresses and output ports eg. an Ethernet frame with a destination MAC address 000c:1234:4567 is dispatched to Port 2.
VOQs | Virtual Output Queues. This is a very high speed memory modules that performs frame queueing in silicon. Queueing is needed to ensure that the fabric is not overrun in the outbound direction. Also, packets arriving from the fabric must not overrun the MAC interfaces.
Fabric | Interface chip to the switch fabric. For the NX7K, this is a five interface connection to the fabric modules on a clos switch design.
10G MAC | Media Access Control for 10 gigabit Ethernet port. Think of it as the signal encoder for SFP interface.
Linksec | Encryption processor for line rate cryptography if you are using Linksec.

## Slide 50: Separation of duty
Decouple control plane and data plane
Routing tables built in control plane
  Static configuration or routing protocols (OSPF, RIP, BGP, etc.)
Downloaded to data plane/forwarding engine where it is called forwarding information base (FIB)
Notes: Why?

## Slide 51: Control Plane
More like a regular computer running multiple programs

## Slide 52: Data Plane - ASIC
Speed, speed, speed! But how fast?
No need to look at entire packet

## Slide 53
Event | Latency
L1 cache hit | 0.5 nano seconds (ns)
L2 cache hit | 7 ns
Main memory hit | 100 ns
Disk seek | 10,000,000 ns
Time to process line rate packet (10Gbps) | ~ 70 ns

## Slide 54
88 bytes

## Slide 55: Layer 2 Forwarding
Hardware MAC learning – can learn ~100K entries
SMAC lookup to learn new <mac, vlan> entries
DMAC lookup to figure which port to exit
How would you design this?

## Slide 56: Layer 3 Forwarding
Longest Prefix Match (route lookup)
  Hit returns next hop (interface)
How would you design this?
Lots of other stuff (buffering, quality of service, firewalls, security features…)

## Slide 57
Prefix/Mask | TCAM entries
101/3 | 101X
111/3 | 111X
10/2 | 10XX
0/0 | XXXX  Default

## Slide 58: Layer 3 Sundry
Lots of other stuff (buffering, quality of service, firewalls, security features…)