REGISTER ALLOCATION  ( 3/11/05)

The getreg function :

The function getreg returns the location L to hold the value of x for the assignment

x:=y op z .

The algorithm for getreg:

1) If the name y is in a register , that holds the value of  no other names (in other words no   other names point to the same register as y does), and y is not live and has no next use  after the execution of y = x op z, then

  - return L.

  - Update the address descriptor of y , so that y is no longer in L.

2) Failing (1), return an empty register for L if there is one.

3) Failing (2),	if x has a next use in the block, or if op requires a register then

a.	find an occupied register R.

b.	MOV(R,M) if value of R is not in proper M. If R holds value of many variables, generate a MOV for each of the variables.

4) Failing (3), select the memory location of x as L.

Example:

d := (a-b) + (a-c) + (a-c)

| Statements | Code generated | Register descriptor | Address descriptor |
| --- | --- | --- | --- |
| t = a-b | MOV a, R0 SUB b,R0 | R0 contains t | t in R0 |
| u= a-c | MOV a, R1 SUB c,R1 | R0 contains t R1 contains u | t in R0 u in R1 |
| v= t+u | ADD R1,R0 | R0 contains v R1 contains u | u in R1 v in R0 |
| d= v+u | ADD R1,R0 MOV R0,d | R0 contains d | d in R0 d in R0 and memory |

Note that cost of this code can be reduced from 12 to 11 by generating MOV R0,R1 immediately after the instruction MOV a,R1.

The guiding force behind a good program is the strategy of efficient allocation of registers.

A simple design is to keep fixed number of registers for each purpose like:

1) Base address

2) Stack

3) Arithmetic Operations

The simple design compensates for the inefficient utilization by this strategy.

Example of usage of registers across blocks:

d,f,b,c

# Text boxes

a = b+c  ; e = a+f  ;       d = d-b;

f = a –d;

b=d+f ;    e= a-c;

b = d+c;

c,d,e,f,b

c,d,e,f,b

d,e,f,b

a,c,d,e

a,c,d,f