## Slide 1
<number>
Matrix representation of physical systems- Associated errors
Somnath Roy
somnath.roy@mech.iitkgp.ac.in
Department of Mechanical Engineering

## Slide 2
Matrix representation of physical systems
System of linear equations with multiple variables can be expressed as matrix equation
Physical systems with multiple degree of freedom can give matrix equations
Rate equations in a continuum can be converted to matrix equations by Taylor series like approximations
Continuum ideally have infinite degree of freedom, but can be approximated with a large finite number of discrete variables.

## Slide 3
<number>
Differential equation -> Difference equations (addition-subtraction operations)
Discretization – journey from analytical to numerical
One-dimensional steady heat conduction
Steady heat flow, constant conductivity
x=0
x=1
Boundary conditions

## Slide 4
<number>
Discretization – Finite difference method
x=0
x=1
1 2 3 4 5 6 7 8
dx
T(x-dx) T(x) T(x+dx)
uniform mesh

## Slide 5
Adding (A) and (B)
approximation error (of order 2)

## Slide 6
Discretization error
is the largest term in the error.
The rod has a length L=1
dx=1/N <1
So, (dx)2 <<1
As we will increase number of grid points, error will be smaller

## Slide 7
<number>
Non-Uniform mesh
x=0
x=1
1 2 3 4 5 6 7
rdh
T(x-dh) T(x) T(x+rdh)
dh

## Slide 8
Finite difference method- equation system
1 2 3 4 5 6 7 8 9
T=0
T=1
So, a set of linear equations are obtained for temperature at points 2,3,….8
dx
T=0
T=1
Uniform mesh

## Slide 9
Matrix representation
It is important to have boundary conditions
If both boundary has T=0, trivial solution T=0 at all points are obtained
Banded sparse matrix—
Tridiaginal matrix

## Slide 10
Two dimensional problem
Can be expressed as a matrix equation after sequential numbering of (i,j) points
x
y

## Slide 11
Method based on Taylor series expression of difference terms
Unknown variable is solved at fixed number of pre-defined discrete points or nodes
Error is bounded by the truncated term of difference approximation
This error is a function of spacing between consecutive nodes or grid-spacing
Finite difference method

## Slide 12
Banded diagonal matrix is obtained
For Laplace/Poisson equation gives tridagonal matrix in 1D
Pentadiagonal in 2D and septadiagonal in 3D!
For uniform mesh, matrix is symmetric
Finite difference method

## Slide 13
Finite volume method
PDEs are expressed as flux differenced between two surfaces
Heat generation: Q.dx.dy.1= (qn+qs)*dx.1+ (qw+qe)*dy.1
Or, Q=0= (qn+qs)/dy+ (qw+qe)/dx
0 =((TN-TP)/dy+(TS-TP)/dy)/dy+ ((TE-TP)/dx+(TW-TP)/dx)/dx

## Slide 14
Finite element method
Entire domain is discretized into a number of smaller elements
A trial/test solution is assumed within each element
Error is estimated from the trial solution
Total error inside each element is integrated and the integral is minimized to get a trial solution with least error, i.e., maximum accuracy
Advantage: Mathematically sound, element shape can vary, complex
geometries can be easily handled
Disadvantage: Difficult mathematics, discretization along flow direction is difficult

## Slide 15
Discretization error (due to difference approximation, vanishes as grid-spacing decreases or no. of discrete point (N) increases)
Round-off error (precision of the computer to round of after few decimal places)
increases with increase in no of calculation steps or with higher no of discrete points (N)
22/7=3.1428571428571428571428571428571
Errors associated

## Slide 16
Total error
Δx (grid spacing)
Δx =L/N
Grid independent solution preferred grid size
Optimal solution

## Slide 17
Validation and verification
Validation: Comparison with available
experimental/ analytical results
Verification: verifying the accuracy of the code
error is 2nd (or higher) order function
of grid-spacing